## Slide 1: PEER DESIGN REVIEW Powered Dobsonian Telescope Nathan Wiley
Submitted in partial fulfillment of the requirements of CST471
ESET Senior Project, Oregon Institute of Technology.

## Slide 2: Agenda:
The Problem and Solution
Designs, Features, and Progress
Block Diagram
Part Selection
Calculations
Cost
Schedule

## Slide 3: The Problem:
Telescopes are not automated enough!
Need to be present to punch in coordinates
Cold
Clunky
Outdated

## Slide 4: The Solution:
Make a telescope that you can control from your couch!

## Slide 5: Design & Features:
Requirements (Very condensed)
1. Shall pivot a telescope (accuracy to 3600 arcseconds / 1 degree)
2. Shall be able to keep accurate time
3. Shall use a control system
4. Shall have a network interface
5. Shall use a display
Stretch goals
1. May have a camera
2. May use RTC module
3. May include GPS module
4. May include Wi-Fi and Ethernet
5. May include cooling system

## Slide 6: Design process and progress:

## Slide 7: Block Diagram:
Raspberry PI
Stepper Driver
Stepper Driver
Vertical Motor
Horizontal Motor
Client
Ethernet
Or Wifi
Power supply
Camera

## Slide 8: Part Selection: Board

## Slide 9: Part Selection: Gearing
DFM Engineering, Inc Engineering Article: Comparing Telescope Drive Technologies

## Slide 10: Part Selection: Motorization Type

## Slide 11: Part Selection: Motorization Type

## Slide 12: Part Selection: Stepper Motor Driver

## Slide 13: Calculations:
1,296,000 arcseconds per 360 degrees, 1 revolution
Stepper motor has 200 steps per revolution, 1.8 degrees per step
100:1 Planetary gear input is attached to motor output
4:1 Belt drive input is attached to planetary gear output
1,296,000 / (200)*(100)*(4) = 16.2 arcseconds (0.0045°) per step
With microstepping it could be even higher precision!

## Slide 14: Cost:
Still Need:
Belt and pulley
Camera
Adjustable zoom eyepiece

## Slide 15: Schedule - Fall Term Chart

## Slide 16: Schedule - Tasks for Fall Term
Done
Design Tube Rings
Build Tube Rings
Design Base
Build Base
Research motor types
Research processors
Decide motor type
Decide processor
Order motors
Order power supply
In progress
Finish non motorized telescope
Design motor housing
Design motor gearing
Familiarize with processor / board
Not Started
Familiarize with controlling motors

## Slide 17: Broad Schedule:

## Slide 18: Questions?